# Notes on TrinketLightMeter project
Pin connections for the Trinket to the 16x2 LCD Display
Trinket BATT	No connection
Trinket GND	GND LCD, TCS34725
Trinket #4	No connection
Trinket	#3	No connection
Trinket RST	No connection
Trinket	5V	5V LCD, TCS34725
Trinket	#2	SCL LCD, TCS34725, with 10K pullup resistor
Trinket	#1	No connection
Trinket	#0	SDA LCD, TCS34725, with 10K pullup resistor
Trinket	USB	No connection

The TCS34725 can only communicate on I2C address 0, so set the LCD to 1 (solder bridge). After examining the code on the TCS34725 driver, that device has I2C address 0x29 locked in, so there was no conflict after all.

Converted the Adafruit_TCS34275 driver to a TinyTCS34275 by replacing all the calls to Wire with calls to TinyWireM. Got it working correctly once I had all of the libraries ONLY in the libraries folder of the Arduino folder.

First calibration tests are showing drift in the sensor and that there appears to be no correlation between the calculated value of lux given in the example code and the clear reading from the sensor. Need to understand this to make use of the tool.

Data sheet specs. At again 16x, atime 0XF6
- @465nm, clear channel typical 13.8 counts μW/cm2
- @525nm, clear channel typical 16.6 counts μW/cm2
- @615nm, clear channel typical 19.5 counts μW/cm2
Dark count is 5.
Max count is 65,535.
Alternative gains are 1x, 4x and 60x.
From “Liquid Crystal – Applications and Uses”
“Incidence is a new generic term which has been coined to describe the measurement of flux incident on a surface (i.e., flux per unit area of the receiving surface). In photometric terms, incidence is called illuminance (Eν) and is defined as the quotient of the luminous flux incident on an infinitesimal element of the surface containing the point under consideration divided by the area of that surface element.

 E sub %nu = %PHI sub %nu over a = I sub %nu over d ^ 2
The unit is lumens per unit area. If the area is measured in square feet, the most common unit is lumen per sq. ft or footcandle (fc) If the area is measured in square meters, the unit is called lumens per square meter or lux. One footcandle is 10.76 lux.

In radiometric terms, “incidence” is called irradiance and is defined in units of “radiant power per unit area”. Typical units are watts per square meter (Wm-2) and microwats per square centimeter.

With 700ms integration time and 1x gain, a reading of 4000 corresponds to:
R sub "blue" = 4000/13.8/16/29.2 = .62 %mu Wcm^-2 newline R sub "green" = 4000/16.6/16/29.2 = .52 %mu W cm^-2 newline R sub "red" = 4000/19.5/16/29.2 = .44 %mu W cm^-2 newline